## Slide 1: EEE 111 Diode Applications
Topic 2 (Chapter 2)

## Slide 2
RS = 1 kW
VS = 15 V
A circuit like this can be solved in several ways:
Use the first approximation or ideal equivalent circuit
Use the second approximation or simplified equivalent circuit or constant voltage drop model
3. Use the diode’s characteristic curve (load line analysis)
Solving Diode Circuits

## Slide 3
2.2 Load-Line Analysis
The load line plots all possible combinations of diode current (ID) and voltage (VD) for a given circuit. The maximum ID equals E/R, and the maximum VD equals E.
The point where the load line and the characteristic curve intersect is the Q-point, which identifies ID and VD for a particular diode in a given circuit.

## Slide 4: Load-Line Analysis
The solution found by load-line analysis is similar to that obtained by a simultaneous solution of
  (assuming this theoretical diode curve is very close to the actual curve.)
The mathematics involved would require the use of nonlinear techniques that are beyond the needs and scope of this course.

## Slide 5: EXAMPLE 2.1
For the series diode configuration of Fig. 2.3a, employing the diode characteristics of Fig. 2.3b, determine:

## Slide 6
Forward current in mA
0
5
10
15
0
2.5
5.0
7.5
10.0
12.5
15.0
17.5
20.0
Source voltage in volts
ISAT =
1 kW
15 V
15 V
1 kW
= 15 mA
VCUTOFF = 15 V
Q
Q is the operating point or quiescent point
Load line
.
Demonstration of Load Line Analysis

## Slide 7
2.3 Series Diode Configurations
The forward resistance of the diode is usually so small compared to the other series elements of the network that it can be ignored.
In general, a diode is in the “on” state if the current established by the applied sources is such that its direction matches that of the arrow in the diode symbol, and VD ≥ 0.7 V for silicon, VD ≥ 0.3 V for germanium, and VD ≥ 1.2 V for gallium arsenide.

## Slide 8: 2.3 Series Diode Configurations

## Slide 9: Reversing the diode

## Slide 13
Assume 1.8V forward voltage drop for the red LED.

## Slide 14
For an actual practical diode, when
ID = 0 A, VD = 0 V (and vice versa) No Bias condition

## Slide 16: 2.4 PARALLEL AND SERIES–PARALLEL CONFIGURATIONS
The methods applied for series diode configurations can be extended to the analysis of parallel and series–parallel configurations.
For each area of application, simply match the sequential series of steps applied to series diode configurations.

## Slide 20: 2.5 AND/OR GATES

## Slide 21: Quiz 2
Use 11th edition of the textbook
Syllabus: 2.2, 2.3 and 2.4
Examples:
  Chapter 2: 2.4 – 2.13
Problems:
  Chapter 2: 5, 6, 7, 8, 9, 10, 11, 12

## Slide 22: Rectifier Circuits
One important application of diode is the rectifier
  Converts AC to DC
  Used to make dc power supplies
Figure: Block diagram of a dc power supply

## Slide 23: Input AC signal
Rectifier input: Sine, square, triangular waves
Sine wave: Positive and negative half cycle
.

## Slide 24
2.6 Half-Wave Rectification
The diode conducts only when it is forward biased, therefore only half of the AC cycle passes through the diode to the output.
The DC output voltage is 0.318Vm, where Vm = the peak AC voltage.

## Slide 25
2.6 Half-Wave Rectification
The process of removing one-half the input signal to establish a dc level is called half-wave rectification
Ideal Approximation

## Slide 26: The effect of using a real diode

## Slide 27: The Half-Wave Rectifier

## Slide 28
which is a difference that can certainly be ignored for most applications.

## Slide 29
PIV (PRV)
Where PIV = Peak inverse voltage
PRV = Peak reverse voltage
Vm = Peak AC voltage
The diode is only forward biased for one-half of the AC cycle. It is also reverse biased for one-half cycle.
It is important that the reverse breakdown voltage rating of the diode be high enough to withstand the peak, reverse-biasing AC voltage.
          PIV (or PRV) > Vm

## Slide 30
2.7 Full-Wave Rectification
  Half-wave: Vdc = = 0.318Vm
  Full-wave: Vdc = = 0.636Vm
Full-wave rectification: output for both positive and negative half cycle
Full-wave rectification produces a larger DC output:
The rectification process can be improved by using a full-wave rectifier circuit.

## Slide 31
Full-Wave Rectification
A full-wave rectifier with four diodes that are connected in a bridge configuration
Bridge Rectifier

## Slide 32: The effect of using a real diode

## Slide 33
Full-Wave Rectification
Requires two diodes and a
center-tapped transformer.
(+) half cycle: ON; OFF
(-) half cycle: OFF; ON
  VDC = 0.636Vm
Center-Tapped Transformer Rectifier
Needs a bigger transformer, because the peak is only half the secondary voltage.

## Slide 34: Summary of Rectifier Waveforms
Half-Wave Rectifier
Full-Wave Rectifier
Bridge Rectifier

## Slide 35
Summary of Rectifier Circuits
Vm = the peak AC voltage
Rectifier | Ideal VDC | Realistic Si VDC
Half Wave Rectifier | VDC= 0.318Vm | VDC = 0.318(Vm – 0.7V)
Bridge Rectifier | VDC = 0.636Vm | VDC = 0.636(Vm – 2(0.7 V))
Center-Tapped Transformer Rectifier | VDC = 0.636Vm | VDC = 0.636(Vm – 0.7 V)
In the center tapped transformer rectifier circuit, the peak AC voltage is the transformer secondary voltage to the tap.

## Slide 37: The Rectifier with a Filter Capacitor - The Peak Rectifier

## Slide 38: The Peak Rectifier with a Load Resistor – A More Practical Circuit

## Slide 39: The full-wave peak rectifier
The ripple is smaller than half-wave rectifier
Ripple voltage inversely proportional to filter capacitor

## Slide 40: 2.8 Diode Clippers
Clippers are networks that employ diodes to “clip” away or removes a portion of an input signal without distorting the remaining part of the applied waveform.
The half-wave rectifier is an example of the simplest form of diode clipper—one resistor and a diode.
Depending on the orientation of the diode, the positive or negative region of the applied signal is “clipped” off.
Two general categories of clippers: series and parallel.
  Series clippers: The diode in series with the load
  Parallel clippers: The diode in parallel to the load

## Slide 41
Diode Series Clippers
The diode in a series clipper “clips” any voltage that does not forward bias it:
Series Clipper: Diode and Load resistance () in series
Clips negative portion of the input: Negative Clipper
A reverse-biasing polarity
A forward-biasing polarity less than 0.7 V (for a silicon diode)

## Slide 42
Biased Clippers
Adding a DC source in series with the clipping diode changes the effective forward bias of the diode.
Biased Clipper: A DC source also present in the circuit
Series Clipper
Negative Clipper

## Slide 43
Positive half cycle
Diode FB/ON/Short
KVL:
Negative half cycle
Diode RB/OFF/Open

## Slide 44
Parallel Clippers
DC biasing can be added in series with the diode to change the clipping level.
The diode in a parallel clipper circuit “clips” any voltage that forward biases it.
Parallel Clipper: Diode and Load resistance () in parallel
Clips positive portion of the input: Positive Clipper

## Slide 45
Positive half cycle
Diode RB/OFF/Open
Negative half cycle
Diode FB/ON/Short

## Slide 47
Summary of Clipper Circuits

## Slide 48
Summary of Clipper Circuits

## Slide 49
2.9 Clampers
A clamper is a network constructed of a diode, a resistor, and a capacitor that shifts a waveform to a different dc level without changing the appearance of the applied signal.
Clamping networks have a capacitor connected directly from input to output with a resistive element in parallel with the output signal.
  The diode is also in parallel with the output signal but may or may not have a series dc supply as an added element.
  Peak-peak or swing of input and output must be same.

## Slide 50
2.9 Clampers
Check in which cycle diode is FB/ON?
Positive half cycle.
Positive half cycle: Capacitor charges. Diode FB/ON.
Find capacitor voltage (). Find output ().
KVL: .
Negative half cycle: Capacitor discharges. Capacitor voltage and polarity will not change.
Diode RB/OFF. Find output ().
KVL: .
Peak-peak or swing of input and output
must be same

## Slide 52
Summary of Clamper Circuits

## Slide 53
Biased Clamper Circuits with sine input
The DC source lets you adjust the DC camping level.
The input signal can be any type of waveform such as a sine, square, or triangle wave.

## Slide 54
2.11 Zener Diodes
The Zener is a diode that is operated in reverse bias at the Zener Voltage (Vz).
RB: When Vi  VZ
  The Zener is on
  Voltage across the Zener is VZ
  Zener current: IZ = IR – IRL
  The Zener Power: PZ = VZIZ
RB: When Vi < VZ
  The Zener is off
  The Zener acts as an open circuit
Zener diode works exactly similar as Semiconductor diode in Forward Bias (FB)

## Slide 55: Approximate equivalent circuits for the Zener diode in the three possible regions of application
Forward Bias (FB)
Reverse Bias (RB): OFF
Reverse Bias (RB): ON

## Slide 61
Please write the following things on your exam paper and take your CLEAR picture with the First Page.
You can take the picture and save it on your phone NOW.
Write your Name and NSU ID.
Write the Course Name, Course Code and section number. Analog Electronics I (EEE111.8)
Write the following pledge. "I affirm that I have not given or received any unauthorized help on this exam, and that all work are my own".
Clearly sign below the pledge.
Give page numbers for ATLEAST 8 pages

## Slide 62
= 6th digit of your NSU ID
Example: If 1632345042 is your ID, then = 4.
You MUST have to submit before 12:50 PM
You can submit PDF or JPG
If you miss any page, send me a private comment ASAP