## Slide 1: BJT AC Analysis
Topic 5 (Chapter 5)

## Slide 2: 5.2 AC Amplification
After a transistor has been biased with the Q point near the middle of the load line, we can couple a small ac voltage into the base (input).
  This will produce an ac collector voltage (output).
  The ac collector voltage looks like the ac base voltage, except that it's a lot bigger.
    In other words, the ac collector voltage is an amplified version of the ac base voltage.
The invention of amplifying devices, first vacuum tubes and later transistors, was crucial to the evolution of electronics.
  Without amplification, there would be no radio, no television, and no computers.

## Slide 3
The amplitude of vce is larger than that of vbe by the voltage gain Av
BJT amplifier biased at a point Q
A small signal voltage vbe is applied
The output signal vce appears superimposed on the dc collector voltage VCE

## Slide 4: Base-biased amplifier
AC input is applied into base
Coupling capacitors are used to block DC
  The reactance of a coupling capacitor is small for AC signal
Amplified and inverted output at the collector.
AC output coupled to the load ()
Voltage Gain:

## Slide 5
+30 V
5 kW
1 MW
bdc = 100
100 kW
100mV
DC analysis gives: IB = 29.3 mA, IC = 2.93 mA and VC = 15.35 V
Coupling capacitors are used to block DC
0
+ 15.35 V
0
+0.7 V
A base-biased amplifier with capacitive coupling

## Slide 6
t
t
t
29.3 mA (Only DC)
2.93 mA
15.35 V
Base current
Collector current
Collector voltage
Waveforms
(Only AC)
Only DC
Only AC
DC + AC

## Slide 7
{
The coupling capacitor
Capacitor current,
DC Analysis: is fixed.
Open
AC Analysis: Reactance
. Short
Large
R
SHORT
R
OPEN
1. For ac analysis, the capacitor is a short.
2. For dc analysis, the capacitor is open.

## Slide 8: BJT Amplifier Analysis
Superposition Theorem (DC + AC analysis)
DC voltages and currents are calculated mentally by opening capacitors: DC Analysis (Chapter 4)
The AC signal is coupled via a coupling capacitor
Coupling capacitor: couples between BJT & input AND BJT & output
The bypass capacitor causes an AC signal to appear across the base-emitter junction and provides higher gain
Bypass capacitor: Need in DC. Not need in AC.

## Slide 9
+1.1 V
+10 V
1 kW
10 kW
2.2 kW
3.6 kW
100 kW
100 mV
+6.04 V
0
0
+1.8 V
VDB Amplifier
Coupling Capacitors
Bypass Capacitor

## Slide 10
ib
bDC =
IC
IB
bac =
ic
The dc current gain is given as:
The ac current gain is given as:
Use CAPITAL letters for dc quantities
and lowercase letters for ac.

## Slide 11
re’ =
26 mV
IE
Formula for ac emitter resistance
Derived by using solid-state physics and calculus:
Diode AC Resistance, Chapter 1
is AC emitter resistance
is DC emitter current

## Slide 12: 5.3 BJT TRANSISTOR MODELING
Transistor Circuit
AC Equivalent Circuit: After the removal of the dc supply and insertion of the short-circuit equivalent for the capacitors.
Redrawn for small-signal ac analysis

## Slide 13: Transistor AC models
AC equivalent circuit for a transistor
Simulates how a transistor behaves when an ac signal is present
There are two models commonly used in small signal AC analysis of a transistor:
    re model
      T model and p type models are widely used
    Hybrid equivalent model (h parameter model)

## Slide 14: 5.4 The Transistor Model (The Input Equivalent Circuit)
BJT similar to two diodes, emitter-base (FB) and collector-base (RB)
Transistor Model: Diode between Emitter and Base
E
B

## Slide 15: The re Transistor Model (The BJT Equivalent Circuit – T Model)
BJT similar to two diodes, emitter-base (FB) and collector-base (RB)
Transistor Model: AC resistance () between Emitter and Base (input/ base side)
Output/ collector side: ; output current = input current
Output side: Current dependent current source ( diamond shape)

## Slide 16
Deriving p model from T model
re’
ic
ie
ib
vbe = iere
= (b+1) ibre
zin(base)

## Slide 17
The p model of a transistor
is based on zin(base) = bre:
bre
Ic=bib
ie
ib
zin(base)

## Slide 18: Overview of re Transistor Models (T and p Model)
T Model
p Model
c
e
b

## Slide 19: re model including effects of ro
In practical transistors, collector current depends on collector voltage
Ideally, ( Open circuit)
Practically, is very high but not infinity

## Slide 20: BJT Amplifier AC analysis
Superposition theorem (DC + AC analysis)
Perform a complete DC analysis (Chapter 4)
Short all coupling and bypass capacitors for ac signals
Visualize all DC supply voltages as grounds
Replace the transistor by its p or T model
Draw the AC equivalent circuit

## Slide 21
5.5 Common-Emitter
Fixed-Bias
Configuration
  AC equivalent
re model

## Slide 22
Common-Emitter Fixed-Bias Calculations
Input
impedance:
Output
impedance:
Voltage gain:
Current gain:

## Slide 23
1. Short all coupling and bypass capacitors for ac signals
2. DC supply voltages as grounds
3. Replace the transistor by its p or T model
Model: CE
T model: CB
4. Draw the AC equivalent circuit

## Slide 25
INPUT
OUTPUT

## Slide 26
5.6 Common-Emitter Voltage-Divider Bias
re model requires you to determine , re, and ro.

## Slide 27
5.6 Common-Emitter
Voltage-Divider Bias
Input impedance
Output impedance
Voltage gain
Current gain

## Slide 30
Common base PNP: T model
Input: emitter; output: collector
Output Current: input current
Example 5.8: Common Base BJT Amplifier

## Slide 31
Example 5.8: Common Base BJT Amplifier

## Slide 32
5.16 Cascaded Systems
To get more gain, a cascaded amplifier can be used.
The overall voltage gain: AV = AV1AV2
Stage 1
AV1
Stage 2
AV2
vin
RL
vout
zin(stage 2)
The output of one amplifier is the input to the next amplifier
The DC bias circuits are isolated from each other by the coupling capacitors