## Slide 1: Field-Effect Transistors
Topic 6 (Chapter 6)

## Slide 4: Basic Difference Between BJT and FET
The BJT is a current-controlled device
The FET is a voltage-controlled device.

## Slide 5
FETs vs. BJTs
    BJTs are bipolar. FETs are unipolar.
    FETs are voltage controlled devices. BJTs are current controlled devices.
    FETs have higher input impedance. BJTs have higher gain.
4. FETs are less sensitive to temperature variations and are better suited for integrated circuits.
5. FETs are smaller than BJTs.
6. FET have faster switching speed than BJT.
  Similarities:
    Both are Transistors
    Amplifiers
    Switching devices
    3 terminal devices
  Differences:

## Slide 6
FET Types
JFET: Junction FET (Not in our syllabus. Not used NOW)
MOSFET: Metal–Oxide–Semiconductor FET
  D-MOSFET: Depletion MOSFET
  E-MOSFET: Enhancement MOSFET

## Slide 9: MOSFET TYPES
Two types:
  Depletion type
  Enhancement type
Both of the above types have two sub-types:
  N-channel or simply n-type (also called NMOS in short)
  P-channel or simply p-type (also called PMOS in short)

## Slide 10: Some Facts..
The name MOSFET is derived from its physical structure.
  Metal Oxide Semiconductor Field Effect Transistor
However, MOSFET’s gates do not actually use any “metal”, polysilicon is used instead.
Another name for MOSFET is insulated gate FET, or IGFET.

## Slide 11: ENHANCEMENT-TYPE MOSFET
E-MOSFET

## Slide 12
E-Type MOSFET Construction
The Gate (G) connects to the p-type substrate via a thin insulating layer of silicon dioxide (SiO2)
There is no channel!
The n-type material lies on a p-type substrate that may have an additional terminal connection called the Substrate (SS) or Body (B)
The Drain (D) and Source (S) connect to the to n-type regions.

## Slide 13: Channel formation in the n-channel enhancement-type MOSFET

## Slide 14
The enhancement-type NMOS transistor with a positive voltage applied to the gate
An n channel is induced at the top of the substrate beneath the gate

## Slide 15
minimum

## Slide 16: Field-Effect
The gate and the channel region of the MOSFET form a parallel-plate capacitor
  The oxide layer acts as the capacitor dielectric
The channel conductivity and the current that flows through the channel is determined by the electric field in the channel
  Caused by an applied gate voltage, vGS
  This is the origin of the name “field-effect transistor” (FET)
  A current flows when a voltage vDS is applied
  Potential difference created by vDS
  Channel created by vGS

## Slide 17
An NMOS transistor with > and with a small applied
The depletion region is not shown (for simplicity)

## Slide 19: Change in channel and depletion region with VDS increasing and a fixed value of VGS
fixed
increases
decreases
Channel width
decreases at
drain

## Slide 24
E-Type MOSFET Operation
The enhancement-type MOSFET (E-MOSFET) operates only in the enhancement mode.

## Slide 25
E-Type MOSFET Transfer Curve
Where, VT = the E-MOSFET threshold voltage
k, a constant, can be determined by using values at a specific point and the formula:

## Slide 26: EMOSFET Current Equation
Off Region ( < ) OR ( = )
Linear/Triode/Ohmic Region ( < ) & (>)
Saturation Region ( ) & ( > )
= Transconductance parameter (A/V2)
Overdrive or Effective voltage

## Slide 27: EMOSFET Current Problem
For an enhancement NMOS, = 1 mA/V2, = 3 V.
(a) = 2 V, = 10 V; (b) = 5 V, = 0 V
(c) = 5 V, = 1 V; (d) = 5 V, = 6 V
The NMOS is in which region? Why? Find , and . Write unit.
(a) = 2 V = 3 V. OFF Region.
. Always
(b) = 5 V = 3 V, BUT: = 0 V.OFF Region.
. Always

## Slide 28: EMOSFET Current Problem
(c) = 5 V = 3 V. 0 V.
Linear/Ohmic/Triode Region ( )
. Always
(d) = 5 V = 3 V. 0 V.
Saturation Region ( )
. Always

## Slide 29
PMOS transistors Enhancement Type
Similar to the NMOS transistor
  except that all semiconductor regions are reversed in polarity

## Slide 30
MOSFET Symbols
The symbols try to reflect the actual construction of the device.
The dashed line between drain and source is chosen to reflect the fact that a channel does not exist between the two under no-bias conditions.
It is, in fact, the only difference between the symbols for the depletion-type and enhancement-type MOSFETs.
NMOS: source current leaves the NMOS.
PMOS: source current enters the PMOS.

## Slide 31
6.7 Depletion-Type MOSFET Construction
The Drain (D) and Source (S) connect to the to n-type regions.
  The n-typed regions are connected via an n-channel.
  The n-channel is connected to the Gate (G) via a thin insulating layer of silicon dioxide (SiO2).
The n-type material lies on a p-type substrate or body that may have an additional terminal connection called the Substrate (SS).

## Slide 32: Basic Operation and Characteristics
Figure: n-Channel depletion-type MOSFET with VGS = 0 V and applied voltage VDD.
Figure: Reduction in free carriers in a channel due to a negative potential at the gate terminal.

## Slide 33
Basic MOSFET Operation
A depletion-type MOSFET can operate in two modes:
  Depletion and Enhancement modes

## Slide 34
Depletion Mode Operation (D-MOSFET)
  When VGS = 0 V, ID = IDSS
  When VGS < 0 V, ID < IDSS
  The formula used to plot the transfer curve for a JFET applies to a D-MOSFET as well:

## Slide 35
Enhancement Mode Operation
Of D-MOSFETs
(ID > IDSS)
VGS is now positive
The formula used to plot the transfer curve still applies:

## Slide 37
D-Type MOSFET Structures
P-channel DMOS N-channel DMOS
Same as Enhancement EMOS.
Only difference: N/P channel exists between drain and source before applying any voltage

## Slide 38
D-Type MOSFET Symbols
The symbols try to reflect the actual construction of the device.
The lack of a direct connection (due to the gate insulation) between the gate and the channel is represented by a space between the gate and the other terminals of the symbol.
The vertical line representing the channel is connected between the drain and the source and is “supported” by the substrate.
Two symbols are provided for each type of channel to reflect the fact that in some cases the substrate is externally available, whereas in others it is not.
For most of our analysis, the substrate and the source will be connected and the lower symbols will be employed.

## Slide 39: JFET Characteristics
Unipolar device (one polarity of charge carrier – no minority carriers)
High input impedance
Source and drain are interchangeable in most low-frequency applications
Two diodes: gate-source and gate-drain
For normal operation the gate-source diode is reverse-biased

## Slide 40
JFET Construction
The n-channel is the more widely used of the two.
There are two types of JFETs:
  n-channel
  p-channel

## Slide 41
N-Channel JFET Symbol

## Slide 42
JFET Operating Characteristics
VGS = 0 V (zero), VDS increasing to some positive value
  VGS < 0 V (negative), VDS at some positive value
  Ohmic region: Voltage-controlled resistor
There are three basic operating conditions for a JFET:

## Slide 43
JFET Characteristics: VGS=0V
  Even though the n-channel resistance is increasing, the current from source to drain (ID) through the n-channel is increasing because VDS is increasing.
Three things happen when VGS = 0 V and VDS increases from 0 V to a more positive voltage:
  The size of the depletion region between p- type gate and n-channel increases.
  Increasing the size of the depletion region decreases the width of the n-channel, which increases its resistance.

## Slide 44
JFET Operation: VGS=0V

## Slide 45
JFET Characteristics
Current in channel (ID) drops to 0 A.
Before pinch-off, ID increases with VDS.
After pinch-off, further increases in VDS do not cause ID to increase. It is called “Saturation”.
With VGS = 0 V, VDS continually increases, eventually the depletion region gets so large that it pinches off the channel.

## Slide 46: PRACTICALLY At Pinch-Off, ID is Not Zero!
The term pinch-off is a misnomer in that it suggests the current ID is pinched off and drops to 0A.
  However, ID maintains a saturation level defined as IDSS
In reality, a very small channel still exists, with a current of very high density.
Why zero ID is not possible at pinch-off? The absence of a drain current would remove the possibility of different potentials along the n-channel to establish the varying levels of reverse bias along the p–n junction.
  The result would be a loss of the depletion region distribution that caused pinch-off in the first place.

## Slide 47
JFET Operating Characteristics,VGS<0V
As VGS becomes more negative, the depletion region increases.

## Slide 48
JFET Operating Characteristics
ID eventually drops to 0 A. The value of VGS that causes this to occur is designated VGS(off).
At high levels of VDS, the JFET reaches a breakdown situation. ID increases uncontrollably if VDS > VDSmax, and the JFET is likely destroyed.
As VGS becomes more negative:
The JFET experiences pinch-off at a lower voltage (VP).
ID decreases (ID < IDSS) even when VDS increases

## Slide 49
Voltage-Controlled Resistor
The region to the left of the pinch-off point is called the ohmic region.
The JFET can be used as a variable resistor, where VGS controls the drain-source resistance (rd).
As VGS becomes more negative, the resistance (rd) increases.
A good first approximation:

## Slide 50
P-Channel JFETs
The p-channel JFET behaves the same as the n-channel JFET.
The only differences are that the voltage polarities and current directions are reversed.

## Slide 51
P-Channel JFET Characteristics
Also note that at high levels of VDS the JFET reaches a breakdown situation: ID increases uncontrollably if VDS > VDSmax.
  The depletion region increases, and ID decreases (ID < IDSS)
As VGS becomes more positive:
ID eventually drops to 0 A (when VGS = VGSoff)
The JFET experiences pinch-off at a lower voltage (VP).

## Slide 52: JFET Symbols

## Slide 53: JFET Operation Summary

## Slide 54
JFET Transfer Characteristics
JFET input-to-output transfer characteristics are not as straightforward as they are for a BJT.
BJT:  indicates the relationship between IB (input) and IC (output).
JFET: The relationship of VGS (input) and ID (output) is a little more complicated:

## Slide 55
0
2
4
6
8
10
-4
-3
-2
-1
VGS in volts
ID in mA
JFET Transfer Characteristics
(Transconductance curve)
ID = IDSS
1-
VGS
VGS(off)
(
)
2

## Slide 56
JFET Transfer Curve

## Slide 59: Complementary MOS or CMOS
Most widely used of all the IC technologies
  Applies to both analog and digital circuits
CMOS is preferred over BJT in digital applications:
  Less power.
  Higher input impedance.
  Scaling is easier

## Slide 60
CMOS Devices
CMOS (complementary MOSFET) uses a p-channel and n-channel MOSFET; often on the same substrate.
Another arrangement is also possible in which an n-type body is used and the n device is formed in a p well

## Slide 61: Digital Logic Inverters
Most basic element in design of digital circuits.
Figure: A logic inverter operating from a dc supply VDD.

## Slide 62
CMOS Logic Design: CMOS Inverter
Input 1, Output 0
Input 0, Output 1

## Slide 63: FET Biasing
(We will limit our discussion to only E-MOSFET.)

## Slide 68: Mathematical Vs. Graphical Approach
The relationship between input VGS and output ID is nonlinear, which complicates the mathematical approach to the dc analysis.
We want to design Amplifier with MOSFET
MOSFET will be in Saturation Region
Current is constant in Saturation region
A graphical approach is less accurate but quicker
We will use graphical solutions rather than mathematical solutions.

## Slide 69: FET General Relationships for DC Analysis

## Slide 70
Plotting The E-MOSFET Transfer Curve
Once k is defined, other levels of ID can be determined for the chosen values of VGS
Determining about 3 to 4 points enables drawing the device transfer characteristics.

## Slide 71
Voltage-Divider Biasing
Plot the line and the transfer curve to find the Q-point using these equations:
= 0; =

## Slide 72
Voltage-Divider Bias Q-Point
(E-MOSFET)
Network: Plot the line using
    VGS = VG , ID = 0 A
    ID = VG / RS , VGS = 0 V
Device: Using the following values from the spec sheet, plot the transfer curve:
    VGSTh, ID = 0 A
    VGS(on) , ID(on)
The point where the line and the transfer curve intersect is the Q-point.
Using the value of ID at the Q-point, solve for the other circuit values.

## Slide 74
For the NMOS below, and
Draw the device/characteristics curve and load line of the NMOS. Show the Q-point in the graph.
Find , , , and .
Step 0: Give appropriate current directions for the 3 terminals.
Step 1: Drawing Load Line from KVL at Gate-Source.
Step 2: Draw device/ characteristics curve from MOSFET current equation.
Step 3: Get -point from the intercept of Load Line and device/characteristics curve.
Step 4: Find from KVL at Drain-Source

## Slide 75
For the NMOS below, and
Draw the device/characteristics curve and load line of the NMOS. Show the Q-point in the graph.
Find , , , and .

## Slide 76
For the NMOS below, and
Draw the device/characteristics curve and load line of the NMOS. Show the Q-point in the graph.
Find , , , and .

## Slide 77
G
Step 1: Drawing Load Line from KVL at Gate-Source:

## Slide 78
Step 2: Drawing device/characteristics curve from MOSFET current equation:

## Slide 79
;
, Always

## Slide 80
Step 4: Find from KVL at Drain-Source
We know:

## Slide 81
Special Case: If is not given. But is given
Given, at

## Slide 82: FET Amplifiers
(We will limit our discussion to only E-MOSFET.)

## Slide 84
E-Type MOSFET AC Equivalent
gm and rd can be found in the specification sheet for the FET.
An open-circuit between gate and drain–source channel

## Slide 85: Determining gm
The constant k can be determined from a given typical operating point on a specification sheet

## Slide 86
Common-Source Voltage-Divider Bias
The input is applied to the gate and the output is taken from the drain.
There is a 180º voltage phase shift between input and output.

## Slide 87
Calculations
Input impedance:
Output impedance:
Voltage gain:

## Slide 90
Thank You!
It was great having you in the class!
Best of luck!