## Slide 1: Bipolar Junction Transistors
Topic 3 (Chapter 3)

## Slide 2: Bipolar Junction Transistor (BJT)
A semiconductor device that can amplify (enlarge) electronic signals such as radio and television signals
The transistor has led to many other semiconductor inventions including the integrated circuit (IC)
  Backbone of modern civilization
Bipolar means “two polarities” - electrons and holes

## Slide 3: BJT Device Structure
NPN
PNP
Emitter has highest doping
Collector has highest width
Base has lowest width and doping: Base current is very small. very small

## Slide 4: The Structure of BJT Transistors in ICs
The collector virtually surrounds the emitter region
The device is not symmetrical, and thus the emitter and collector cannot be interchanged.
Figure: A more realistic (but still simplified) cross section of an npn BJT

## Slide 5
Discrete Component BJT Construction
pnp
npn
BJT: Three terminals. Emitter, Base, Collector.
BJT: Two Junctions.
Emitter – Base Junction (EB)
Collector – Base Junction (CB)
EB | CB | 
FB | FB | ON: Saturation mode
FB | RB | Amplifier: Active mode
RB | RB | OFF: Cutoff mode
RB | FB | Inverter

## Slide 6: Unbiased transistor
Three doped regions: emitter, base, and collector
Two pn junctions: emitter-base and base-collector
  Like two back-to-back connected diodes
Two types: NPN or PNP
Silicon or germanium

## Slide 7
COLLECTOR (medium doping)
BASE (light doping)
EMITTER (heavy doping)
N
P
N
The bipolar junction transistor has 3 doped regions.

## Slide 8: Biased transistor
BJT in Active mode
Forward bias the emitter diode
Reverse bias the collector diode
BJT works as an Amplifier

## Slide 9
N
P
N
VCE
VCC
RC
RB
VBB
VBE
In a properly biased NPN transistor, the emitter electrons
diffuse into the base and then go on to the collector.

## Slide 10: Purposes of Different Transistor Regions
The heavily doped emitter emits or injects its free electrons into the base
The lightly doped base also has a well-defined purpose: to pass emitter-injected electrons on to the collector
The collector is so named because it collects or gathers most of the electrons from the base

## Slide 11: Electron Movement
If VBE is greater than the emitter-base barrier potential (0.7 V for Si), emitter electrons () will enter the base region
These electrons can flow in either of two directions.
  They can flow out of the base through the base terminal or Recombination ()
  They can flow into the collector ()

## Slide 12: Which way the free electrons in the base region go?
Most continue on to the col­lector
  Why?
    The base is lightly doped and very thin
    The light doping means that there are very few majority carriers
    The very thin base means that the free electrons have only a short distance to go to reach the collector
    The positive voltage (reverse voltage) applied to the collector pulls them towards the collector
    For these reasons, almost all the emitter-injected electrons pass through the base to the collector.
  Only a few free electrons will recombine with holes in the lightly doped base

## Slide 13: Summary of Carrier Flow in a Biased NPN Transistor
VBB forward biases the emitter diode
  Forces the free electrons in the emitter to enter the base
The thin and lightly doped base gives almost all these electrons enough time to diffuse into the collector
These electrons flow through the collector, through RC and into the positive terminal of the VCC voltage source
N
P
N
VCE
VCC
RC
RB
VBB
VBE

## Slide 14
Transistor Operation
With the external sources, VEE and VCC, connected as shown:
  The emitter-base junction is forward biased
  The base-collector junction is reverse biased

## Slide 15
Currents in a Transistor
Emitter current is the sum of the collector and base currents:

## Slide 16
Carrier flow in a pnp transistor
The collector current is comprised of two currents:
Emitter current is the sum of the collector and base currents:

## Slide 17: Transistor Connections
There are three useful way to connect a transistor:
CE (common emitter) – most widely used
CC (common collector)
CB (common base)

## Slide 18
Common-Emitter
Configuration
The emitter is common to both input (base-emitter) and output (collector-emitter) circuits.
The input is applied to the base and the output is taken from the collector.

## Slide 19
Common-Emitter Amplifier Currents
  IE = IC + IB IC =  IE
Actual Currents
When IB = 0 A the transistor is in cutoff, but there is some minority current flowing called ICEO.
    where ICBO = minority collector current
      ICBO is usually so small that it can be ignored, except in high power transistors and in high temperature environments.
Ideal Currents
IC =  IE + ICBO

## Slide 20: Transistor Current Gain
Current Gain () =
The ratio of collector current to base current is current gain (βdc)
Current gain is typically 100 to 300

## Slide 21
Conventional flow
Electron flow
IC
IB
IE
IC
IB
IE
IE = IC + IB
IC @ IE
IB << IC
adc =
IC
IE
bdc =
IC
IB

## Slide 22
Beta ()
In DC mode:
In AC mode:
 represents the amplification factor of a transistor.

## Slide 23
Beta ()
Determining  from a Graph

## Slide 24
Beta ()
Relationship between amplification factors  and  :
Relationship Between Currents:

## Slide 30
CE Transistor Characteristics
Collector or Output Characteristics
Base or Input Characteristics
To fully describe the behavior of a BJT, two sets of characteristics are required:
  Driving point or input characteristics
  Output side or output characteristics

## Slide 31
Common-Base Configuration
The base is common to both input (emitter–base) junction and output (collector–base) junction of the transistor.

## Slide 32
Common-Base Amplifier
Input Characteristics
This curve shows the relationship between of input current (IE) to input voltage (VBE) for three output voltage (VCB) levels.

## Slide 33
Common-Base Amplifier
This graph demonstrates the output current (IC) to an output voltage (VCB) for various levels of input current (IE).
Output Characteristics

## Slide 34
Operating Regions
Active
Operating range of the amplifier.
Cutoff
The amplifier is basically off. There is
voltage, but little current.
Saturation
The amplifier is fully on. There is current, but little voltage.

## Slide 35
Transistor Amplifier
Voltage Gain:
Currents and Voltages:

## Slide 36
Common-Collector Configuration
The input is on the base and the output is on the emitter.

## Slide 37
Common-Collector Configuration
The characteristics are similar to those of the common-emitter amplifier, except the vertical axis is IE.

## Slide 38
Power Dissipation
Common-collector:
Common-base:
Common-emitter: